## Slide 1: Computers Logic and CPU
Patrice Koehl
Computer Science
UC Davis

## Slide 2: Computers
Logic: acting on information
Elements of a Computer
The Central Processing Unit (CPU)

## Slide 3: Computers
Logic: acting on information
Elements of a Computer
The Central Processing Unit (CPU)

## Slide 4
The concept of pressure
When we remove the block, what is the effect on pressure?

## Slide 5
Decreases
The concept of pressure
When we remove the block, what is the effect on pressure?

## Slide 6
Electrical pressure: voltage
Switch
If switch is off (0) (equivalent to
the presence of the block)
Voutput=Vcc high (i.e. 1)
If switch is on (1) (equivalent to
the absence of the block)
Voutput<<Vcc low (i.e. 0)
“Inverter”

## Slide 7
The transistor
Base
Collector
Emitter
A transistor can be used as an
electronic switch:
if Vbase is high, the current
“flows” between the emitter and
the collector
(switch is on)
If Vbase is low, the current
does not pass
(switch is off)

## Slide 8
The not gate
Input: 0
1
Input: 1
0
Input | Output
0 | 1
1 | 0

## Slide 9
Input A | Input B | Output
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
0 | 0 | 1
The not-and (NAND) gate

## Slide 10
The AND gate
Input A | Input B | Output
1 | 1 | 1
1 | 0 | 0
0 | 1 | 0
0 | 0 | 0

## Slide 11
The not-or (NOR) gate
Input A | Input B | Output
1 | 1 | 0
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1

## Slide 12
The OR gate
Input A | Input B | Output
1 | 1 | 1
1 | 0 | 1
0 | 1 | 1
0 | 0 | 0

## Slide 13
http://en.wikipedia.org/wiki/Logic_gate

## Slide 14: Computers
Logic: acting on information
Elements of a Computer
The Central Processing Unit (CPU)

## Slide 15
Control
Memory
Input
Output
CPU
The CPU consists of three parts:
the Arithmetic Logic Unit (ALU)
The Control Unit
Memory
The Central Process Unit (CPU)
ALU

## Slide 16
The Fetch/Execute Cycle
The CPU cycles through a series of operations or instructions,
organized in a cycle, the Fetch/Execute cycle:
Instruction Fetch (IF)
Instruction Decode (DP)
Data Fetch (DF)
Instruction Execute (IE)
Result Return

## Slide 17
Step 1: Instruction Fetch
Fetch instruction from memory position 2200:
Add numbers in memory positions 884 and 428, and
store results at position 800

## Slide 18
Step 2: Instruction Decode
Decode instruction:
Defines operation (+), and set memory pointers in ALU

## Slide 19
Step 3: Data Fetch
Fetch data:
Get numbers at memory positions 428 and 884: 42 and 12
and put in ALU
PC: 2200

## Slide 20
Step 4: Instruction Execution
Execute:
Add numbers 42 and 12 in ALU: 54
PC: 2200
[800]

## Slide 21
Step 5: Return Result
Return:
Put results (54) in position 800 in memory
PC: 2200

## Slide 22
Possible operations
Computers can only perform about 100 different types of operations; all other operations must be broken down into simpler operations among these 100.
Some of these operations:
Add, Mult, Div
AND, OR, NAND, NOR, …
Bit shifts
Test if a bit is 0 or 1
Move information in memory
…

## Slide 23
Repeating the F/E cycle
Computers get their impressive capabilities by performing
many of these F/E cycles per second.
The computer clock determines the rate of F/E cycles per
second; it is now expressed in GHz, i.e. in billions of cycles
per seconds!
Note that the rate given is not an exact measurement.

## Slide 26
(http://en.wikipedia.org/wiki/Accelerating_change)

## Slide 27
(http://en.wikipedia.org/wiki/Accelerating_change)

## Slide 28: Computers
Logic: acting on information
Elements of a Computer
The Central Processing Unit (CPU)

## Slide 29
CPU
Input devices
Output devices
Storage
Computer: basic scheme

## Slide 30
CPUs are getting smaller, and can include more than one “core” (or processors).
CPUs get hot, as their internal components dissipate heat: it is important to add a heat sink and fans to keep them cool.
The Central Process Unit (CPU)

## Slide 31
The motherboard:
backbone of the computer
Slot for memory:
RAM
Slot for CPU
Input/Output: Keyboard, Mouse,…
Extension cards: Video, sound, internet…
Hard drive connectors
Power supply connector

## Slide 32
Communications on the mother board